KPilot
Use Case Specification: Conduit Syncing Requirements
Version: 1.12

This page is intentionally left blank.
Revision History
Version	Date	Author	Description
	2007-05-26	Jason 'vanRijn' Kasper	Initial document version to baseline document structure and sample flows and steps.
	2007-05-28	Bertjan Broeksema	Did a first attempt to write the hotsync flow.
	2007-05-28	Bertjan Broeksema	Writed the other flows and the conflict resolution options.
	2007-05-30	Bertjan Broeksema	Changed the main flow after discussion with vanRijn.
	2007-06-01	Bertjan Broeksema	Did a bunch of restyling and added some additional information to the business rules.
	2007-06-06	Bertjan Broeksema	Added a bit of logic to ensure that no data is lost when something bad happens during sync. / Added CUD counter. / Added Test mode. / Specified “clean up” a bit more.
	2007-06-11	Jason 'vanRijn' Kasper	Added explanation and clarification to Business rules section regarding data stores. / Added description and clarification for First Sync scenario and its importance for the ID Mapping. / Added placeholders for copy XX to XX flows / Cleaned up and expanded on other existing flows.
	2007-06-12	Jason 'vanRijn' Kasper	Added Copy XX to XX flows
	2007-06-18	Bertjan Broeksema	Added Database proxies
	2007-06-19	Jason 'vanRijn' Kasper	Cleanups after paper-review / Adding table row ID's to everything that makes sense for easy discussion and follow / Changing all numbered lists to headers for ease of reference and maintenance (phew) / Putting in standard main and alternate flows sections / Using document fields for title and version for footers and first page
	2007-06-22	Jason 'vanRijn' Kasper	Clarifying some of the interactions of the Proxy database / Fixing section references (5.5->6.5, etc.)
	2007-07-03	Bertjan Broeksema	Changed two values in table 6.3.1. There was a “-” used in two cases where it was about “no record” in stead of unchanged record.
	2007-07-17	Bertjan Broeksema	Added information about archived records.
	2007-07-26	Bertjan Broeksema	Changed the fullsync slow a bit / Added two extra cases in record syncing

Table of Contents

# Description and Purpose
This document is intended to describe the interactions, responsibilities, and flows that KPilot record-based conduits have. It is initially a study of the existing conduit flows and steps, and is intended to unify them and allow for abstraction of common code, and to establish a firm foundation in the form of a set of common code that is implemented and used across all of KPilot's conduits.
# Glossary
ID	Term	Description
	Palm Database	This is the Palm database that contains the records that the conduit will be synchronizing with the PC. It is opened directly from the Palm device. This is also loosely referred to as “Palm” and “Handheld” below.
	Last Synced Palm Database	This is a local copy of the Palm database, kept in Kpilot's $HOME/.kde/share/apps/kpilot/conduits/<Username>/<Database>.pdb. It is the exact image of what KPilot last synced with. At the end of every successful sync, the Conduit will ensure that this database is the mirror image of the Palm database that will exist on the Palm after the sync is done.
	PC Data Store	This is the data that exists in whatever format the user keeps it in on the PC. This can be a variety of formats, including flat files, iCal, vCal, ICS, XML, etc.
	Proxy Database	A wrapper for PC data stores and Palm databases which keeps track of all creates, updates and deletes that are planned for a data store and applies them to the real data stores after the Conduit has made sure that no data loss is occuring.
	ID Mapping	Each conduit will keep track of the mapping that must exist between the Palm's data record identifiers (using an unsigned long), and the PC's record identifiers (can be a variety of sources, including iCal UIDs, for example). This mapping will be kept in XML files in $HOME/.kde/share/apps/kpilot/conduits/<Username>/mapping/<Conduit>-mapping.xml.
	CUD Counter	Creates, Updates, Deletes counter. This class keeps track of the changes that are made to the Palm database and PC data store during a synchronization. It is used to both report on the number of changes that are made to both data stores and to prevent severe data loss by measuring the volatility of these changes.

# Preconditions and Postconditions
## Preconditions
### The user has a Palm device and wishes to synchronize its contents with the conduits that KPilot provides.
### The Palm data store that the user wishes to sync with is record-based (i.e. Addressbook or Datebook).
## Postconditions
### Conduit has successfully synchronized all data between all 3 data stores (on-Palm database, PC data store, and Backup Palm database), as well as the PC-based ID Mapping.
### All 3 data stores contain the same data now.
### The ID Mapping file contain correct cross-key information and is record-count-equal and id-content-equal to the Backup Palm database.
# Main Flow
## HotSync
### This flow starts when the user initiates a synchronization with KPilot.
### KPilot begins the synchronization process and runs through its initial steps. These steps are not detailed here, but include verifying that the UserID that is on the Palm matches the UserID that KPilot is configured to synchronize with.
### KPilot instantiates our record-based conduit (“Conduit”, hereafter).
### Conduit ensures that Palm connection is kept alive by means of a repeating “tickle” that is sent to the Palm every 10 seconds in a separate thread, until the Conduit has completed synchronization.
### Conduit loads settings from configuration file.
### Conduit reads the AppInfo block of the palm database.
### Conduit opens all 3 data stores and applies business rules for opening data stores (See table 1).
### The conduit creates a proxy database for each of the data stores. This proxy database will be used as a temporary workplace during sync such that any and all changes that need to be made to the data stores will first be made in the proxy. Each proxy database will contain all records (modified and unmodified) from the data stores.
#### Each proxy database creates a CUD Counter for tracking Creates, Updates, and Deletes, and sets the beginning record count for each from the respective data store.
### Conduit opens the ID Mapping file and validates it. If the Conduit cannot open an existing ID Mapping file, or if the mapping file is invalid or not in sync with the Backup Palm database, Conduit will perform a First Sync and flow will end there. (See section 6.2 for further details).
### Conduit requests all records, that have the modified flag set, from the proxy database for the Handheld database.
### Conduit Iterates over each of the returned records.
#### Look for corresponding PC record from ID Mapper.
#### Look for corresponding Palm record in Backup data store.
#### Using all 3 records (some may be empty or null if this is a new record), apply rules for record sync (see table 2).
#### Proxy database updates the CUD Counter appropriately with each Create, Update, or Delete.
### Conduit requests all modified records from the proxy database for the PC Data Store.
### Iterate over each loaded record.
#### Look for corresponding Palm record from ID Mapper.
#### Look for corresponding Palm record in Backup data store.
#### Using all 3 records (some may be empty or null if this is a new record), apply rules for record sync (see table 2)
#### Proxy database updates the CUD counter
### Conduit checks the volatility of the changes that have taken place during the sync. Conduit checks both number of changes (Creates, Updates, Deletes) as well as percentage of changes (number of changes divided by beginning record count, unless beginning number is 0 and then it's considered as 100%). If volatility (number or percentage) exceeds threshold configured by user (defaulted to something sensible), the user is warned about the situation and asked to approve the changes.
### If either the changes are within acceptable limits or if the user approves the volatile changes then the Conduit commits the changes made during the synchronization.
#### Reset all "dirty" (modified) flags in data stores.
#### Saves AppInfo blocks which includes any changed Category information.
#### Applies all changes made to Proxy databases to the actual databases.
#### Saves ID mapping information back to disk.
#### Set the last synced time/date and the Last Synced PC in the ID mapper.
#### Copies the Palm database file over the top of the last Backup database file so that they are guaranteed to now be in sync.
### Flow ends.
# Alternate Flows
## First Sync
This flow occurs when:
- The Backup database for this Conduit's palm database does not exist.
- The ID Mapping file for this Conduit does not exist or it is not valid (see section 6.2).

### Flow 4.1.1 through 4.1.8.1 occurs
### Conduit creates a new ID Mapping.
### Conduit loads all records from Handheld (modified and unmodified).
### Conduit loads all records from the PC data store (modified and unmodified).
### Conduit Iterates over each record from Handheld
#### Looks for a match in the PC record set (Conduit does field-wise comparison to establish equality)
##### If a match is not found, add Palm record to PC data store, otherwise use existing PC record.
#### Proxy database updates CUD counter for PC if new record was added to the PC data store.
##### Create mapping between Palm and PC records and add mapping to ID Mapping.
### Conduit Iterates over each record from PC data store that does not have an entry in the ID Map.
#### Since we have already made sure in step 5 that this record will not be field-wise equal to any of the Palm's records, copy record to the Handheld.
##### Proxy database updates CUD counter for Handheld.
#### Create mapping between Palm and PC records and add to ID Mapping.
### Flow 4.1.13 continues
## Full Sync
This flow starts when:
- The Conduit's Last Synced PC ID number does not match the PC ID number that it is currently syncing with.
- It was explicitly requested by the user pressing the Full Sync button in KPilot.
- The setting "always full sync" was selected in the configuration dialog.

### Flow 4.1.1 through 4.1.8.1 occurs.
### Conduit requests all records (modified and unmodified) from Handheld proxy database.
#### Conduit registers which pc records are in sync
### Flow 4.1.11 occurs.
### Conduit requests all records (modified and unmodified) from PC data store proxy.
#### Conduit iterates only over records that are not in sync yet.
### Flow 4.1.14 continues and ends.
## Copy Handheld To PC
This flow occurs when:
- The user selects this as her next synchronization type.
- The user selects this as her default synchronization method.
- Case 6.3.3 or 6.3.4 will have occurred.

### Flow 4.1.1 through 4.1.8.1 occurs.
### Conduit requests all records (modified and unmodified) from Handheld proxy database.
### Conduit requests all records (modified and unmodified) from PC proxy database.
### Conduit iterates over each record from Handheld
#### Looks for a match in the ID Map.
#### If a match is not found, add Palm record to PC data store, otherwise use existing PC record.
#### Proxy database updates CUD counter for PC if record was added.
#### Create mapping between Palm and PC records and add relationship to ID Mapping.
### Conduit then iterates over PC records.
#### If the record is not found in the ID Map, remove it from the PC data store and increment the CUD counter Deleted count.
#### If the record is found in the ID Map, but not present in the Handheld data store, remove it from the PC data store and the ID Mapping and increment the CUD counter Deleted count for the PC.
### Flow continues from 4.1.14 and ends.
## Copy PC To Handheld
This flow occurs when:
- The user selects this as her next synchronization type.
- The user selects this as her default synchronization method.
- Case 6.3.5 or 6.3.6 has occurred.

### Flow 4.1.1 through 4.1.8.1 occurs.
### Conduit requests all records (modified and unmodified) from Handheld proxy database.
### Conduit requests all records (modified and unmodified) from PC proxy database.
### Conduit iterates over each record from PC.
#### Looks for a match in the ID Map.
#### If a match is not found, add PC record to Handheld data store, otherwise use existing Handheld record.
#### Proxy database updates CUD counter for the Handheld if record was added.
#### Create mapping between Palm and PC records and add relationship to ID Mapping.
### Conduit then iterates over Palm records.
#### If the record is not found in the ID Map, remove it from the Handheld data store and increment the CUD counter Deleted count.
#### If the record is found in the ID Map, but not present in the PC data store, remove it from the Handheld data store and increment the CUD counter Deleted count.
### Flow continues from 4.1.14 and ends.
## Test Mode
This flow will not affect any changes to any of the 3 data stores of the ID Mapping file. It is intended to allow for per-conduit testing only.
### Flow 4.1.1 through 4.1.8.1 occurs
### The method test() which must be overloaded by the subclass is called.
### The temporary databases, data store and mapping are removed
# Business Rules
## Opening Data Stores
This section describes what to do when opening of one of the data stores that is used by KPilot fails. These data stores are as follows:
### HH: This is the Handheld database that exists on our user's Palm device.
### PC: This is the user's data as it is stored on the PC. This can be flat files, iCal files, database records, or anything else that the user wishes to store her data in. Mostly this is dictated by the program that the user is using (for example: kaddressbook stores its PC data store in VCF f-iles, korganizer uses ICS files,etc.).
### Backup: This is a Palm database that is a copy of the Palm database that existed on the user's Palm Handheld device when the last sync with KPilot took place. This data store is used to compare the Palm records against each other to determine if they have changed. This is especially important during a full sync to determine whether the HH records have changed, since we cannot rely on the modified flag of the HH records during a full sync.
## ID Mapping File
In addition to these data stores, there is a fourth data store in the form of the ID Mapping file. This XML-formatted file contains vital information for KPilot to perform its HotSync, as it contains the cross-data-source key mappings (for example: HH record “1234455” maps to PC data store ID “ASDF1233fX”). At the end of the synchronization process, the ID Mapping file should contain the same number of records that the Backup Palm database contains, and the Backup Palm record ids should match one-for-one with the ID Mapping file's record ids. If, when the Conduit opens the ID Mapping file, it is either unable to open the ID Mapping file or it finds that the mapping file does not correctly reflect the contents of the Backup Palm database, the Conduit cannot rely on the ID Mapping file and this will result in a First Sync to re-establish the mapping between Palm and PC record identifiers (this mapping only occurs as a result of a successful synchronization between Palm and PC data stores).
The ID Mapping file will be considered valid if the following conditions are true:
1. The number of entities/records that exist in the ID Mapping file match the number of records in the Backup Palm database. This excludes the mappings that have the “archived” flag set.
2. Every record id that is in the Backup Palm database is in the ID Mapping file.
If the above conditions are not found to be true then the Conduit must discard the ID Mapping file and re-establish it with a First Sync.
## Open/Fail Data Store Scenarios
The following table represents the possible open/fail conditions with the 3 primary data stores and the resulting actions taken by the Conduit.
Table 1: Opening data stores
ID	HH	PC	Backup	Action
6.3.1	open	open	open	Hot Sync (or Full Sync when pc id's are different, when configured or explicitly requested by user)
6.3.2	open	open	fail	First Sync. The user has data on both her Handheld and PC, but there is no Backup Palm database for us to do a HotSync.
6.3.3	open	fail	open	Copy Handheld To PC. The user has data on her Handheld, and because the Backup Palm database exists on her PC, it shows that she has synchronized with KPilot before. For some reason, the PC data store cannot be opened, so we will re-create it from the Palm.
6.3.4	open	fail	fail	Copy Handheld to PC. The user has data on her Handheld, but because we cannot find a Backup Palm database on the PC, we assume that she has not synchronized with KPilot before. No PC data store is found, so we'll create one for her from her Palm.
6.3.5	fail	open	open	Copy PC to Handheld. Because we have a Backup Palm database on the PC, we know that our user has synced with KPilot before. This condition appears to be caused by a Palm device reset or error. We will create a new Palm database from our user's PC data store.
6.3.6	fail	open	fail	Copy PC to Handheld. This condition appears to indicate that our user has never synchronized with KPilot (at least not for the current Palm User). Create the Palm database from the PC data store.
6.3.7	fail	fail	open	Emit error message and stop flow. This is an erroneous condition because neither side has any data to sync in either direction.
6.3.8	fail	fail	fail	Emit error message and stop flow. This is an erroneous condition because neither side has any data to sync in either direction.

## Record Synchronization During a First Sync.
The following conditions are to be met by the Conduit's First Sync flow.
### It will work on all records from both the Palm database and the PC data store, regardless of their modified flags/state.
### It will produce a fresh (or refreshed, in case it is out of sync) ID Mapping file that provides the Conduit with a one-to-one mapping (1..1) between PC records and Palm records.
### Rather than doing a full, bi-direction copy, resulting in n+m records on both sides as a result, the First Sync flow will iterate through both complete sets of data and check for field-wise equality. Assuming the Conduit is able to find PC records that are field-wise equal to Palm database records, the result will be n+m-x records, where “x” would be the number of field-wise equal records.

## Record Synchronization
This table describes the rules for syncing two records. '-' means an unmodified record, 'N' means a new record, 'D' means a deleted record, 'X' means no record and '~' means different from backup record but no flags set. Modified is different for a full sync and a hotsync. When doing a hotsync the conduit trusts the flags of the record to reflect the state of the record. In a full sync a record is different when the data of the record is different from the backup record.
Table 2: Record syncing
Case	HH	PC	Action
6.5.1	-	-	unchanged, just sync if first time or full sync
6.5.2	N	X	no record matching the alm ID in the backupDB / data store yet => add record to data store
6.5.3	M	-	record is in backupDB, unchanged in data store => modify in data store and in backupDB
6.5.4	D	-	deleted on Palm, exists in backupDB and data store => delete from datastore and backupDB
6.5.5	X	N	no or invalid mapping record in data store => add to palm and / backupDB
6.5.6	-	M	valid mapping exists => modify on Palm
6.5.7	-	D	Record in backupDB, but not in data store => delete from Palm and backupDB
6.5.8	N	N	Can't find out (the two records are not correlated in any way, they just have the same data!!
6.5.9	M	M	Record exists on Palm and there is a mapping for the ID CONFLICT => ask the user what to do or use a configuration setting
6.5.10	D	M	Record exists on Palm and there is a mapping for the ID CONFLICT => ask the user what to do or use a configuration setting
6.5.11	M	D	Record exists on Palm and there is a mapping for the ID CONFLICT => ask the user what to do or use a configuration setting
6.5.12	D	D	already deleted on both, no need to do anything.
6.5.13	-	X	Add to pc on full sync (ignored on hotsync).
6.5.14	X	-	Add to hh on full sync (ignored on hotsync).
6.5.15	~	-	Copy on full sync changes to pc
6.5.16	-	~	Copy on full sync changes to hand held
6.5.17	~	~	Copy changes depending on conflict resolutionsettings.
6.5.18	D	X	Record created and deleted on Palm between last hotsync. Delete from handheld.

Note: When a record gets removed from the handheld the conduit checks if the record is also archived. If it is then the conduit doesn't remove the record from the pc data store and sets the archived flag in the mapping for this record. Archived records don't get synced anymore.
# Conflict resolution
When a conflict arises in one of the described flows the conduit should be able to handle all of the following possibilities:
### Ask the user which record to use.
### Do nothing (Skip the record)
### The record on the Handheld overrides
### PC record overrides
### Use the values of the last sync (if possible)
### Use both entries.