KPilot
Use Case Specification: Conduit Syncing Requirements
version: 1.6
Revision History
Version	Date	Author	Description
1.0	2007-05-26	Jason 'vanRijn' Kasper	Initial document version to baseline document structure and sample flows and steps.
1.1	2007-05-28	Bertjan Broeksema	Did a first attempt to write the hotsync flow.
1.2	2007-05-28	Bertjan Broeksema	Writed the other flows and the conflict resolution options.
1.3	2007-05-30	Bertjan Broeksema	Changed the main flow after discussion with vanRijn.
1.4	2007-06-01	Bertjan Broeksema	Did a bunch of restyling and added some additional information to the business rules.
1.5	2007-06-06	Bertjan Broeksema	Added a bit of logic to ensure that no data is lost when something bad happens during sync. / Added CUD counter. / Added Test mode. / Specified “clean up” a bit more.
1.6	2007-06-11	Jason 'vanRijn' Kasper	Added explanation and clarification to Business rules section regarding data stores. / Added description and clarification for First Sync scenario and its importance for the ID Mapping. / Added placeholders for copy XX to XX flows / Cleaned up and expanded on other existing flows.

Table of Contents

# Description and purpose
This document is intended to describe the interactions, responsibilities, and flows that KPilot record-based conduits have. It is initially a study of the existing conduit flows and steps, and is intended to unify them and allow for abstraction of common code, and to establish a firm foundation in the form of a set of common code that is implemented and used across all of KPilot's conduits.
# Glossary
Term	Description
Palm Database	This is the Palm database that contains the records that the conduit will be synchronizing with the PC. It is opened directly from the Palm device.
Last Synched Palm Database	This is a local copy of the Palm database, kept in Kpilot's $HOME/.kde/share/apps/kpilot/conduits/<Username>/ directory.
PC Data Store	This is the data that exists in whatever format the user keeps it in on the PC. This can be a variety of formats, including flat files, iCal, vCal, ICS, XML, etc.
ID Mapping	Each conduit will keep track of the mapping that must exist between the Palm's data record identifiers (using an unsigned long), and the PC's record identifiers (can be a variety of sources, including iCal UIDs, for example). This mapping will be kept in XML files in $HOME/.kde/share/apps/kpilot/conduits/<Username>/mapping/.
CUD Counter	Creates, Updates, Deletes counter. This class keeps track of the changes that are made to a palm database or data store.

# Pre and postconditions
## Preconditions
None yet.
## Postconditions
1. Conduit has successfully synchronized all data between all 3 data stores.
2. All 3 data stores contain the same data now.
3. XML Mapping files contain correct cross-key information.
# Flows
## Hotsync (Main flow)
1. This flow starts when the user initiates a synchronization with KPilot.
2. KPilot begins the synchronization process and runs through its initial steps. These steps are not detailed here, but include verifying that the UserID that is on the Palm matches the UserID that KPilot is configured to synchronize with.
3. KPilot instantiates our record-based conduit (“Conduit”, hereafter).
4. Conduit ensures that Palm connection is kept alive by means of a repeating “tickle” that is sent to the Palm every 10 seconds in a separate thread, until the Conduit has completed synchronization.
5. Conduit loads settings from configuration file.
6. Conduit reads the appInfo block of the palm database.
7. Conduit opens data stores, apply business rules for opening data stores (See table 1).
8. Conduit opens the ID Mapping file and validates it. If the Conduit cannot open an existing ID Mapping file, or if the mapping file is invalid or not in sync with the Backup Palm database, Conduit will perform a First Sync and flow will end there. (See section 5.2 for further details).
9. Copy all three data stores and the ID Mapping to a temporary location for synchronization work. All work from this point on will take place on the objects and databases that are in the temporary work location. If any of the data stores were not found, they will be created in the temporary work location.
10. Conduit creates two CUDCounters for tracking Creates, Updates, and Deletes--one for the Handheld one for the PC data store, and sets the beginning record count for each from the respective data store.
11. Conduit loads all records, that have the modified flag set, from the temporary copy of the Handheld database.
12. Iterate over each of the loaded records.
  1. Look for corresponding PC record from ID Mapper.
  2. Look for corresponding Palm record in Backup data store.
  3. Using all 3 records (some may be empty or null if this is a new record), apply rules for record sync (see table 2).
  4. Update the CUD Counter appropriately with each Create, Update, or Delete.
13. Conduit loads all modified records from temporary copy of the PC Data Store.
14. Iterate over each loaded record.
  1. Look for corresponding Palm record from ID Mapper.
  2. Look for corresponding Palm record in Backup data store.
  3. Using all 3 records (some may be empty or null if this is a new record), apply rules for record sync (see table 2)
  4. Conduit updates the CUD counter
15. Conduit cleans up:
  1. Reset all "dirty" flags in Backup and Handheld databases.
  2. Saves AppInfo blocks which includes any changed Category information.
  3. Saves ID mapping information back to disk.
  4. Set end count of both CUD counters.
  5. Set the last synced time/date in the ID mapper and the Last Synced PC.
  6. Copies the Palm database file over the top of the last Backup database file so that they are guaranteed to now be in sync.
16. Conduit checks the volatility of the changes that have taken place during the sync. Conduit checks both number of changes (Creates, Updates, Deletes) as well as percentage of changes (number of changes divided by beginning record count, unless beginning number is 0 and then it's considered as 100%). If volatility (number or percentage) exceeds threshold configured by user (defaulted to something sensible), the user is warned about the situation and asked to approve the changes.
17. Only if the user approves the volatile changes, then the Conduit copies the three data stores and ID mapper (in the temporary directory) to their permanent places and “commits” the sync.
18. Conduit removes temporary data stores and mappings.
19. Flow ends.
## First sync
This flow occurs when:
- The Backup database does not exist.
- The ID Mapping file does not exist or it is not valid (see section 5.2).

1. Flow 4.1.1 through 4.1.10 occurs
2. Conduit creates a new ID Mapping.
3. Conduit loads all records from Handheld (modified and unmodified).
4. Conduit loads all records from the PC data store (modified and unmodified).
5. Conduit Iterates over each record from Handheld
  1. Looks for a match in the PC record set (Conduit does field-wise comparison to establish equality)
  2. If a match is not found, add Palm record to PC data store, otherwise use existing PC record.
  3. Create mapping between Palm and PC records and add mapping to ID Mapping.
  4. Update CUD counter.
6. Conduit Iterates over each record from PC data store that does not have an entry in the ID Map.
  1. Since we have already made sure in step 5 that this record will not be field-wise equal to any of the Palm's records, copy record to the Handheld.
  2. Create mapping between Palm and PC records and add mapping to ID Mapping.
  3. Update CUD counter
7. Flow 4.1.15 continues
## Full Sync
This flow starts when:
- The Conduit's Last Synced PC ID number does not match the PC ID number that it is currently syncing with.
- It was explicitly requested by the user pressing the Full Sync button in KPilot.
- The setting "always full sync" was selected in the configuration dialog.

1. Flow 4.1.1 through 4.1.10 occurs.
2. Conduit loads all records (modified and unmodified) from Handheld.
3. Flow 4.1.12 occurs.
4. Conduit loads all records (modified and unmodified) from PC data store
5. Flow 4.1.14 continues.
6. Flow ends.
## Copy Handheld To PC
This flow will take place solely upon the user's request. The user will explicitly request to have this synchronization take place.
1. Flow 4.1.1 through 4.1.10 occurs.
2. Conduit loads all records (modified and unmodified) from Handheld.
3. Conduit clears ID Mapping file and resets it to empty.
4. Conduit <TODO: FINISH THIS AND NEXT FLOW>
## Copy PC To Handheld
## Test Mode
This flow will not affect any changes to any of the 3 data stores of the ID Mapping file. It is intended to allow for per-conduit testing only.
1. Flow 4.1.1 through 4.1.10 occurs
2. The method test() which must be overloaded by the subclass is called.
3. The temporary databases, data store and mapping are removed
# Business rules
## Opening Data Stores
This section describes what to do when opening of one of the data stores that is used by KPilot fails. These data stores are as follows:
1. HH: This is the Handheld database that exists on our user's Palm device.
2. PC: This is the user's data as it is stored on the PC. This can be flat files, iCal files, database records, or anything else that the user wishes to store her data in. Mostly this is dictated by the program that the user is using (for example: kaddressbook stores its PC data store in VCF files, korganizer uses ICS files,etc.).
3. Backup: This is a Palm database that is a copy of the Palm database that existed on the user's Palm Handheld device when the last sync with KPilot took place. This data store is used to compare the Palm records against each other to determine if they have changed. This is especially important during a full sync to determine whether the HH records have changed, since we cannot rely on the modified flag of the HH records during a full sync.
## ID Mapping File
In addition to these data stores, there is a fourth data store in the form of the ID Mapping file. This XML-formatted file contains vital information for KPilot to perform its HotSync, as it contains the cross-data-source key mappings (for example: HH record “1234455” maps to PC data store ID “ASDF1233fX”). At the end of the synchronization process, the ID Mapping file should contain the same number of records that the Backup Palm database contains, and the Backup Palm record ids should match one-for-one the ID Mapping file's record ids.. If, when the Conduit opens the ID Mapping file, it is either unable to open the ID Mapping file or it finds that the mapping file does not correctly reflect the contents of the Backup Palm database, the Conduit cannot rely on the ID Mapping file and this will result in a First Sync to re-establish the mapping between Palm and PC record identifiers (this mapping only occurs as a result of a successful synchronization between Palm and PC data stores).
The ID Mapping file will be considered valid if the following conditions are true:
1. The number of entities/records that exist in the ID Mapping file match the number of records in the Backup Palm database.
2. Every record id that is in the Backup Palm database is in the ID Mapping file.
If the above conditions are not found to be true then the Conduit must discard the ID Mapping file and re-establish it with a First Sync.
## Open/Fail Data Store Scenarios
The following table represents the possible open/fail conditions with the 3 primary data stores and the resulting actions taken by the Conduit.
Table 1: Opening databases
HH	PC	Backup	Action
open	open	open	Hot Sync (or Full Sync when pc id's are different, when configured or explicitly requested by user)
open	open	fail	First Sync. The user has data on both her Handheld and PC, but there is no Backup Palm database for us to do a HotSync.
open	fail	open	Copy Handheld To PC. The user has data on her Handheld, and because the Backup Palm database exists on her PC, it shows that she has synchronized with KPilot before. For some reason, the PC data store cannot be opened, so we will re-create it from the Palm.
open	fail	fail	Copy Handheld to PC. The user has data on her Handheld, but because we cannot find a Backup Palm database on the PC, we assume that she has not synchronized with KPilot before. No PC data store is found, so we'll create one for her from her Palm.
fail	open	open	Copy PC to Handheld. Because we have a Backup Palm database on the PC, we know that our user has synced with KPilot before. This condition appears to be caused by a Palm device reset or error. We will create a new Palm database from our user's PC data store.
fail	open	fail	Copy PC to Handheld. This condition appears to indicate that our user has never synchronized with KPilot (at least not for the current Palm User). Create the Palm database from the PC data store.
fail	fail	open	Emit error message stop flow. This is an erroneous condition because neither side has any data to sync in either direction.
fail	fail	fail	Emit error message stop flow. This is an erroneous condition because neither side has any data to sync in either direction.

## Record Synchronization During a First Sync.
The following conditions are to be met by the Conduit's First Sync flow.
1. It will work on all records from both the Palm database and the PC data store, regardless of their modified flags/state.
2. It will produce a fresh (or refreshed, in case it is out of sync) ID Mapping file that provides the Conduit with a one-to-one mapping (1..1) between PC records and Palm records.
3. Rather than doing a full, bi-direction copy, resulting in n+m records on both sides as a result, the First Sync flow will iterate through both complete sets of data and check for field-wise equality. Assuming the Conduit is able to find PC records that are field-wise equal to Palm database records, the result will be n+m-x records, where “x” would be the number of field-wise equal records.

## Record Synchronization
This table describes the rules for syncing two records. '-' means an unmodified record, 'N' means a new record, 'D' means a deleted record. Modified is different for a full sync and a hotsync. When doing a hotsync the conduit trusts the flags of the record to reflect the state of the record. In a full sync a record is different when the data of the record is different from the backup record.
Table 2: Record syncing
HH	PC	Action
-	-	unchanged, just sync if first time or full sync
N	-	no record matching the Palm ID in the backupDB / data store yet => add record to data store
M	-	record is in backupDB, unchanged in data store => modify in data store and in backupDB
D	-	deleted on Palm, exists in backupDB and data store => delete from calendar and backupDB
-	N	no or invalid mapping record in data store => add to palm and / backupDB
-	M	valid mapping exists => modify on Palm
-	D	Record in backupDB, but not in data store => delete from Palm and backupDB
N	N	Can't find out (the two records are not correlated in any way, they just have the same data!!
M	M	Record exists on Palm and there is a mapping for the ID CONFLICT => ask the user what to do or use a configuration setting
D	M	Record exists on Palm and there is a mapping for the ID CONFLICT => ask the user what to do or use a configuration setting
M	D	Record exists on Palm and there is a mapping for the ID CONFLICT => ask the user what to do or use a configuration setting
D	D	already deleted on both, no need to do anything.

# Conflict resolution
When a conflict arises in one of the described flows the conduit should be able to handle all of the following possibilities:
1. Ask the user which record to use.
2. Do nothing (Skip the record)
3. The record on the Handheld overrides
4. PC record overrides
5. Use the values of the last sync (if possible)
6. Use both entries.